## Slide 1
Water & Pollution Control
Fats, Oils, and Grease Control Program
www.cityofames.org/FOG
Dustin Albrecht, Environmental Specialist

## Slide 2
What are the reasons for having the FOG Control Program?
  Public Health
  Environmental Concerns
  Financial

## Slide 3
No accumulation of FOG
Free flowing wastewater

## Slide 4
Accumulation of FOG
Obstruction of flow
Non-compliant FSEs

## Slide 5
Large amounts of FOG
Chronic issue
Cleanup is necessary
Penalties
Cost of cleanup ($800 - $1,200)
Fine up to $1,000

## Slide 6
Sources of FOG
Fryer oil, grease/fat from meat, milk, butter, margarine, eggs, lard, salad dressing, creamer, sauces, gravies, ice cream, mayonnaise, syrups, cake icing, sour cream, peanut butter, chocolate, food scraps…

## Slide 7
Why is my business/facility on the FOG Control Program?
  License with DIA
  Connected to City of Ames sanitary sewer
Four types of licenses issued by DIA
  Food Service Establishment
  Retail Food Establishment
  Mobile Food Unit
  Food Processing Plant

## Slide 11
Grease Interceptor Cleaning/Inspection

## Slide 12
Basic Grease Interceptor Operation
 Solids settle to the bottom  FOG floats to the top
Solids
FOG
Water

## Slide 13
How full is too full?
Ames Municipal Code
No more than 35% at any cleaning
Average for all cleanings during compliance period must be 25% or less
Example
% Full = (Fog (ft) + Solids (ft)) / Total Depth (ft)
= ( 0.5 + 1.0 ) / 5.0
= 1.5 / 5.0
= 30%
Too Full

## Slide 14
Filling out the Maintenance Logs
Ames/ISU Ice Arena
1507 Gateway Hills Park
8/6/15
Acme
0.5
1.0
5.0
30%
AMES WPC
None
Amanda Moore
Recreation Coordinator
1/5/2016

## Slide 15
Another Example
Date
 Name of FSE
 Hauler Company & Employee
 Percentage Full
 Disposal Location
 Service Comments

## Slide 16
Common errors/problems
  No records/logs
  Not including all records
  Information missing
  High percentages
  Disposal location
Cannot include too much information

## Slide 17
Time and date of sample is determined by City of Ames W&PC staff.
Grab Sample

## Slide 18
Kitchen Best Management Practices

## Slide 19
Kitchen Best Management Practices (BMPs)
  Train staff
  Scrape/Dry wipe dishes
  Use strainers in sinks
  Dispose of food waste in trash/recycle
  Do not pour oil/grease down drains or toilets
  Limit use of garbage disposals
  Post ‘No FOG’ signs

## Slide 20
Kitchen BMP Checklist

## Slide 21
Staff Training Log

## Slide 23
Cost of Non-Compliance
  Cost of clearing blockages
    $800 - $1,200
  Fine up to $1,000
  Surcharge
    Added to utility bill for 6 months
    Currently $0.00/100 cubic feet
    Collecting data to determine a fair rate

## Slide 24
Timeline of Program
  Two Compliance Periods/year
    January 1 – June 30
    July 1 – December 31
  City staff developing Restaurant Rate in coming months
  Notification of Restaurant Rate in June
  Restaurant Rate added to January 2017 usage

## Slide 25
A-1 Complete | (515) 265-3986
All Clean of Iowa | (515) 334-0670
Anderson Plumbing | (641) 792-5317
Behle, Inc. | (515) 598-5279
Best Portable Toilets | (515) 453-2211
Earl’s Sanitation | (515) 434-2669
Darpro Solutions, LLC | (515) 265-0381
Davis Septic Tank Service | (515) 202-9596
Draintech | (515) 233-3700
Forest Septic | (515) 208-5022
Gudmonson Service | (515) 576-4991
Hydro-Klean | (515) 283-0500
Jim’s Johns | (515) 288-0924
River to River Onsite Septic Solutions | (515) 987-3913
Roto Rooter | (515) 292-9277
Seneca Waste Solutions | (515) 240-2137
Sweet Honey, Inc. | (515) 402-0094
Wiegert Disposal | (641) 764-2389
Grease Hauler Contractors
This list does not include all grease haulers and in no way implies certification or constitutes acceptance of the work of the listed companies. The City of Ames shall not be responsible for the service provided by any companies on this list.

## Slide 26
Dustin Albrecht, Environmental Specialist
Phone: (515) 239-5150
E-Mail: dalbrecht@cityofames.org
FOG Website: http://www.cityofames.org/FOG